## Slide 1
Gamma-ray imaging using GeGI Compton imaging for uranium holdup
Dr. Jeff Preston
Engineering Advisor
Jeff.Preston@pxy12.doe.gov
Notes: Covers tasks A, B, and F

## Slide 2: Compton Imaging
GeGI-5 (double sided cross strip HPGe)
  90mm diameter x ~11mm thick
  3-D Position sensitive detector
  16 channels per side, 32 total
  Depth of interaction
Physics
  Multiple hits independently recorded
  List mode data output
  Energy weighting function determines forward/backward not time of flight
  Simple back projection creates cones
  Cones overlap on unit sphere
  Vendor algorithm determines hotspots
  Multiple gammas may contribute to single image
  Vendor algorithm has capability for rough mass estimation
PHDS GeGI-5

## Slide 3: Compton Imaging
Advantages
  Fast measurement time
  Localization suitable for wide areas
  Full efficiency of detector
  Wide energy range
  Lightweight equipment
Disadvantages
  Limited spatial resolution (application dependent)
  Single gamma energy analysis (multiple energies do not improve results)
  Additional counts do not significantly improve image (may be vendor algorithm specific)
  Low count rates have significant artifacts (requires adjusting response threshold)
Source

## Slide 4: Compton Imaging
Point Source
  Cone projection overlaps in few locations
  Artifacts ideally at minimum
  Single point may show up
  Spurious artifacts often appear/disappear
Area Spread
  Amorphous shapes
  Not necessarily an intensity weighted map
  Analysis overlaid on same 2-D field for one or more gammas (not distinguishing color scheme)
Raw Reconstruction
Result
Raw Reconstruction
Result
Notes: Artifacts sometimes can be removed through selectively filtering image

## Slide 5: Source Construction
Finite Source
  Standards of loose pack DU3O8
    Holdup often other material forms
    Chosen for chemical stability
  Increasing mass/thickness up to infinite thickness
  Material packed inside to limit powder motion
  Gasket to seal box for use outside HCA
  Strong magnets included for mounting sources
  Two sizes
    4.4” x 2.4” x 2”
    2.25” x 2” x 2.1”
  DU not ideal for coded aperture
    Small 186keV contribution
    Sufficient 766/1001keV lines for Compton imaging
YPH-20-904013

## Slide 6: Source Construction
YPH-20-904016
YPH-20-904018
YPH-20-904019
YPH-20-904017

## Slide 7: Compton Imaging
Non-point sources
  1m distance from detector front to source surface
  3D projection onto 2D image
  Area spread ~4” beyond source dimensions in all directions
    <10% of indicated area is real source
  Spurious artifacts outside of source area
U-tube Measurement
  1m distance from detector front to source surface
  Enriched uranium source
  Material settled at bottom of tube
  Similar spread around source
  Caveat: results may be vendor algorithm specific to an extent

## Slide 8: Imaging Improvement
Maximum Likelihood Expectation Maximization (MLEM)
  “GIBLET” created by Keith Bledsoe and Justin Knowles
  Initial effort to use idealized point source data
    Separate runs for Cs-137 and Ho-166m sources
    1m distance
  Python implementation for loops
    Initial trials require overnight runs
  Modification to vectorized math sped up results
    Parallelized code
    Still required several hours on i9 processor
  Images collapsed to point sources
  Method not continued for speed and performance using fieldable systems
  New method will be discussed in later talk
400 pixels, -20cm to 20cm, 12hr runtime

## Slide 9: Imaging Improvement
Bayesian Inference
  Multiple energies from uranium can contribute to solution
    Similar is approach to effective-Z determination
  Multiple energies attenuating independently
  Compton scattering angle linked to energy of incident particle
  Source emitting multiple energies will overlap similarly at true material locations
  Constrain spatial possibilities based from isotope branch emissions
    186keV angles informed by 1001keV angles
    Wide angle scatter and forward scatter bias by energy
  Coded aperture data can also inform Compton results
    Constrain possible locations
    Retrieves a greater depth information than for single 186keV line
  Requires re-creating reconstruction algorithm for speed
    Maintain tracking of error bands from cones as weights
  New method will be discussed in greater detail in later talk
    Compton images to be improved slightly
    Fuse with Coded Aperture to massively improve methods.

## Slide 10: Upcoming Measurements
Y-12 Facility measurements
  Coordinating with NDA and maintenance personnel
  Measure collection of tubes and ducts
    Items currently monitored under UHSP using GGH method
    Long operating history with cleanout masses
    Cleanout is not 100% efficient
    Enriched uranium preference for increased 186keV intensity
  Intending to follow items (Task F: Unattended Monitoring)
    Immediately following cleanout
    During full process cycle
    End with cleanout
  Obtain physical mass collection measurements afterwards
  Acquire list mode data using
    GeGI5 with coded aperture add-on
  Mass estimation comparison with GGH and mass measurements
    PHDS mass estimation routine using Compton
    New routine fusing coded aperture and Compton (to be discussed later)
Notes: Uranium Holdup Survey Program

## Slide 11
DISCLAIMER
This work of authorship and those incorporated herein were prepared by Consolidated Nuclear Security,
LLC (CNS) as accounts of work sponsored by an agency of the United States Government under
Contract DE‑NA‑0001942. Neither the United States Government nor any agency thereof, nor CNS, nor any of their employees, makes any warranty, express or implied, or assumes any legal liability or responsibility to any non-governmental recipient hereof for the accuracy, completeness, use made, or usefulness of any information, apparatus, product, or process disclosed, or represents that its use would not infringe privately owned rights. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise, does not necessarily constitute or imply its endorsement, recommendation, or favoring by the United States Government or any agency or contractor thereof, or by CNS. The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States Government or any agency or contractor (other than the authors) thereof.