## Slide 1
Life Cycle Analysis and Techno Economic Analysis of Marine Carbon Dioxide Removal
Roksana Mahmud1,2, Tommy Schmitt1,2, Derrick Carlson1,2, Sally Homsy1, Matt Jamieson1
1US Department of Energy, National Energy Technology Laboratory (NETL), Pittsburgh PA /Morgantown WV; 2NETL site support contractor
Introduction
Marine Carbon Dioxide Removal (mCDR) is defined as the indirect removal of CO2 from the atmosphere “via an enhancement of the downward air-sea flux of CO2 from the atmosphere to the surface ocean.”
The surface of the ocean is in a constant exchange of CO2 with the atmosphere and represents the largest exchange of CO2 with the atmosphere compared to any other reservoir. The ocean carbon cycle can be seen below.
TEA Methods
Cost and performance estimates for three electrochemical mCDR technologies are presented. The reported costs are in May 2023 dollars.
AM for mCDR, E for electrochemical engineering approach, B for bipolar membrane electrodialysis [BPMED] and C for electrolytic cation exchange membrane [CEM]), and pH shift (1 for acidic, 2 for basic), respectively.
The scale is based on an expected CO2 capture rate of an mCDR facility co-located with an average sized desalination plant in the U.S.
The estimating models are based on a U.S. Florida Atlantic Coast location, and the labor cost was scaled from a Midwest Gulf Coast location.
Conclusion
The preliminary TEA indicates that an LCOC > $1,000/tonne CO2 can be expected for electrochemical mCDR technologies.
The analysis of environmental impacts highlighted that under certain conditions (renewable electricity source) electrochemical mCDR technologies can be net negative.
These results are preliminary, based on limited availability of transparent data.
Ocean Carbon Cycle
Results
Levelized cost of capture (LCOC) comparison.
Sensitivity of mCDR technologies to plant size.
GWP impacts of standalone and co-located marine CDR facilities.
Case | Technology | mCDR Approach | Membrane Process | pH Shift | Capture Rate | CO2 Product
MEB1A | mCDR | Electrochemical Engineering | Bipolar Membrane Electrodialysis (BPMED) | Acidic | 63% | CO2 (g)
MEB2 |  |  |  | Basic | 63% | 
MEC1 |  |  | Electrolytic Cation Exchange Membrane (CEM) | Acidic | 62% | 
Performance Summary | MEB1 | MEB2 | MEC1
Inlet DIC (CO2e), umol/kg (ppmw) | 2,074 (126) | 2,074 (126) | 2,074 (126)
CO2 capture rate, % | 63 | 63 | 62
CO2 product flow rate (pipeline quality), tonne/yr | 13,000 | 13,000 | 13,000
H2 product flow rate, tonne/yr | - | - | 1,481
Total auxiliary load, kWe | 11,994 | 16,455 | 71,754
Preliminary Results, Do Not Cite
Chart: CO2 Product Flow Rate
| 950 | 13000 | 70000 | 100000
MEB1 | 13877.6151 | 8619.0617 | 8076.6415 | 8037.4399
MEB2 | 14190.4875 | 8877.1828 | 8327.0904 | 8288.2067
MEC1 | 26304.0014 | 20812.7436 | 20236.1492 | 20195.1298
N. Wei, The Wei Forward Report II: A radical rethink of the policy framework for investing with impact, 1st ed. Future Planet Capital, 2023. Accessed: Jul. 02, 2023. [Online]. Available: https://static1.squarespace.com/static/582e25f02e69cf5247166bad/t/63f4ac0e0d02fd4a9e021c2c/1676979222143/Wei+Forward+Report+II.pdf
LCA Methods
Boundary: Cradle-to-Gate
Functional unit: 1 kg of CO2 captured
Modeling platform: openLCA v2.1.1
Impact assessment: Traci 2.1 (AR6 100-year time horizon)
Life cycle inventory: TEA material and energy flows
Sensitivity analysis for different electricity sources scenarios.
Disclaimer: This project was funded by the Department of Energy, National Energy Technology Laboratory an agency of the United States Government, through a support contract. Neither the United States Government nor any agency thereof, nor any of its employees, nor the support contractor, nor any of their employees, makes any warranty, expressor implied, or assumes any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, apparatus, product, or process disclosed, or represents that its use would not infringe privately owned rights. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise does not necessarily constitute or imply its endorsement, recommendation, or favoring by the United States Government or any agency thereof. The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States Government or any agency thereof.
Chart: LCOC, 2023 $/tonne CO2
| MEB1 Standalone | MEB1 Co-located | MEB2 Standalone | MEB2 Co-located | MEC1 Standalone | MEC1 Co-located
Capital | 5168.8215 | 394.3619 | 5183.9041 | 393.9282 | 9974.3552 | 2971.64
Fixed | 1975.1969 | 466.6826 | 1979.7003 | 466.4738 | 3491.1138 | 1279.7419
Variable | 746.1 | 152.0482 | 747.7582 | 145.5832 | 3359.4821 | 1532.6502
Electricity | 637.2664 | 333.7298 | 873.9902 | 453.6935 | 3809.6999 | 1931.9837
Total [excluding T&S] | 8527.3847 | 1346.8225 | 8785.3529 | 1459.6786 | 20634.6511 | 7716.0158
Chart: kg CO2e/kg CO2 captured (GWP 100-yr, AR6)
| MEB1 standalone | MEB1 co-located | MEB2 standalone | MEB2 co-located | MEB2 co-located w/ CaCO3 | MEC1 standalone | MEC1 co-located
FRCC | 3.871 | 2.0289 | 5.3099 | 2.7576 | 1.6451 | 23.1464 | 11.7347
2050 U.S. Grid | 3.4016 | 1.783 | 4.6658 | 2.4232 | 1.4458 | 20.338 | 10.311
Current U.S. Grid | 3.9269 | 2.0582 | 5.3866 | 2.7974 | 1.6688 | 23.4809 | 11.9042
Fossil with CCS | 1.479 | 0.77592 | 2.0283 | 1.054 | 0.62941 | 8.8364 | 4.4806
Renewables | 0.25804 | 0.13631 | 0.35312 | 0.18446 | 0.11094 | 1.5318 | 0.77769
Chart: kg CO2e/kg CO2 captured (GWP 100-yr, AR6)
| MEB1 | MEB2 | MEC1
BPMED | 2.9455 | 4.8866 | 0
CEM | 0 | 0 | 11.8801
CO2 membranes | 0.55317 | 0.02032 | 0.26449
CO2 compressor | 0.0023842 | 0.0023842 | 0.0023842
Auxiliary loads | 0.22965 | 0.14031 | 10.8592
Transport | 0.14031 | 0.14031 | 0.14031
Total | 3.871 | 5.1899 | 23.1464